## Slide 1: EMERGENCY LIGHTING PRODUCT
Information based from the Life Safety Code Handbook® explaining the how, what, when, where, and why’s of emergency lighting as well as an in-depth explanation of DSPM’s Life Safety Compliant UL924 products.
SEMINAR
NEMA 1
NEMA 3R
NEMA 4, 4X,12

## Slide 2
LIFE SAFETY CODES I
Fundamental Requirements
Provide adequate safety without dependence on any single safeguard.
Provide an appropriate degree of life safety considering the size, shape, and nature of the occupancy.
Provide for backup or redundant egress arrangements.
Ensure that the egress paths are clear, unobstructed, and unlocked.
Ensure that the exits and egress routes are clearly marked to avoid confusion and provide the cues needed for their effective use.
Provide adequate lighting.
Ensure prompt occupant response by providing early warnings.
Ensure the required systems facilitate and enhance situation awareness.
Ensure the suitable enclosure of vertical openings.
Ensure compliance with applicable installation standards.
Maintain all required features in proper working order.
(From Life Safety Code Handbook, 2012)
(4.5, Life Safety Code Handbook. 2012)

## Slide 3
LIFE SAFETY CODES I
Code Requirements
Means of Egress
Lighting: Where artificial illumination is needed in a building or structure; egress facilities shall be included in the lighting design.
Maintenance: Whenever or wherever any device, equipment, system, condition, arrangement, level of protection, or any other feature is required for compliance with the provisions of this code, such device, equipment, condition, arrangement, level of protection, or other feature shall thereafter be maintained, unless the code exempts such maintenance.
(From Life Safety Code Handbook, 2012)
(Sections 4.5.3.4 and 4.5.8, Life Safety Handbook, 2012)

## Slide 4
EMERGENCY LIGHTING
Emergency illumination shall be provided for at least 90 minutes in the event of failure of normal lighting.
Emergency lighting facilities shall be arranged to provide initial illumination that is not less than an average of 10.8 lux (1 ft-candle) and, at any point, not less than 1.1 lux (0.1 ft-candle), measured along the path of egress at floor level.
Illumination levels shall be permitted to decline to not less than an average of 6.5 lux (0.6 ft-candle) and, at any point, not less than 6.5 lux (0.06 ft-candle) at the end of the 90 minutes. A maximum illumination uniformity ratio of 40 to 1 shall not be exceeded.
(From Life Safety Code Handbook, 2012)
(7.9.2.1, Life Safety Code Handbook, 2012)
Performance of System

## Slide 5
CURRENT SOLUTIONS
Examples of the current solutions used in various locale:
Bug Eyes / Exit Signs

## Slide 6
CURRENT SOLUTIONS
Examples of the current solutions used in various locale:
Battery Pack For Lamps

## Slide 7
CURRENT SOLUTIONS
Examples of the current solutions used in various locale:
Power Generator

## Slide 8
CURRENT SOLUTIONS
Examples of the current solutions used in various locale:
Inverter

## Slide 9
CENTRALIZED
LIGHTING
INVERTER
EXAMPLES

## Slide 10
SINGLE UNIT SINGLE FLOOR

## Slide 11
SINGLE UNIT MULTIFLOOR

## Slide 12
MULTI-UNIT MULTIFLOOR

## Slide 13
OUTDOOR INVERTER

## Slide 14
EMERGENCY LIGHTING INVERTER SERIES

## Slide 15
CORPORATE BROCHURE

## Slide 16
FAMILY LINE OF PRODUCTS
Defender
Series
Cobra
Series
Fortress
Series

## Slide 17
SINGLE PHASE 350W – 2000W

## Slide 18
SINGLE PHASE 2.4KW – 4.2KW

## Slide 19
SINGLE PHASE 4.7KW – 21KW

## Slide 20
THREE PHASE 3KW – 125KW

## Slide 21
SINGLE PHASE 75W – 21KW
Outdoor Lighting Inverter

## Slide 22
THREE PHASE 3KW – 125KW
Outdoor Lighting Inverter

## Slide 23
SINGLE PHASE 75-300W / PATENTABLE TECHNOLOGY

## Slide 24
CENTRALIZED
LIGHTING
INVERTER APPLICATION

## Slide 25
DIMMER BYPASS APPLICATION

## Slide 26
DIMMER BYPASS APPLICATION

## Slide 27
HERE’S WHAT HAPPENED AND HERE’S HOW IT WORKS…
DIMMER BYPASS APPLICATION

## Slide 28
DIMMER BYPASS APPLICATION

## Slide 29
DIMMER BYPASS APPLICATION
The dimmer rack maintains full control over all of the lamps. Dimmer power is at normal luminosity.

## Slide 30
DIMMER BYPASS APPLICATION

## Slide 31
DIMMER BYPASS APPLICATION
BLACKOUT OCCURS
NORMAL OPERATING CONDITIONS

## Slide 32
DIMMER BYPASS APPLICATION
When the dimmer rack power fails, the ECM switches the lamp to inverter power. Once the lights in the theater are at full luminosity, movie patrons can safely exit the room.

## Slide 33
DIMMER BYPASS APPLICATION
ON EMERGENCY BACKUP

## Slide 34
WALL SWITCH BYPASS

## Slide 35
WALL SWITCH BYPASS

## Slide 36
HERE’S HOW IT HAPPENED AND HERE’S HOW IT WORKS…
WALL SWITCH BYPASS

## Slide 37
WALL SWITCH BYPASS

## Slide 38
WALL SWITCH BYPASS
The wall switches maintain full control over all of the lamps. One is utility power and the other is the lighting inverter output. The teacher is lecturing her young students.

## Slide 39
WALL SWITCH BYPASS

## Slide 40
WALL SWITCH BYPASS
When a utility power outage occurs after an explosion, the ECM automatically switches to inverter power providing a paralleled path for the inverter to energize the lamps at full luminosity. Students and teacher can safely evacuate the classroom.

## Slide 41
WALL SWITCH BYPASS

## Slide 42
OUTDOOR INVERTER

## Slide 43
OUTDOOR INVERTER

## Slide 44
OUTDOOR INVERTER
No matter what type of weather disaster is occurring elsewhere, the DSPM’s outdoor inverter will always maintain full luminosity providing safety assurance.

## Slide 45
LIFE SAFETY CODES II
Maintenance Requirements
Whenever or wherever any device, equipment, system, condition, arrangement, level of protection, fire-resistive construction, or any other feature is required for compliance with the provisions with the Code, such device, equipment, system, condition, arrangement, level of protection, fire-resistive construction, or other feature shall thereafter be continuously maintained. Maintenance shall be provided in accordance with applicable NFPA requirements or requirements developed as part of a performance-based design.
Paragraph 4.6.12.1 emphasis the importance of maintaining items required by the Code. It is useless to have an egress door that will not open, a self-closing device that does not close the door, or a sprinkler system with no water.
Also, before taking any life safety features out of service, extreme care needs to be exercised to ensure that the feature is not required, was not originally provided as an alternative or equivalency, or is no longer required due to other new requirements in the current Code.
The Code directs that non-required life safety features that are obvious to the public are to be either maintained or removed to prevent false expectations or a false sense of security by building occupants. For example, if the water supply to a non-required wet standpipe system were permanently shut off because the system piping leaked but the hose and nozzle for occupant use were left attached to the standpipe, an occupant could be endangered while attempting to use the system. If the non-required standpipe system were turned off and abandoned, it would be necessary, as a minimum, to remove all hoses and nozzles and to place prominent signage at each outlet station advising that the system is out of service. The standpipe system piping, however, would not have to be removed.
(From Life Safety Code Handbook, 2012)
(4.6.12.1, Life Safety Handbook, 2012)
(4.6.12.2, Life Safety Handbook, 2012)

## Slide 46
LIFE SAFETY CODES II
Code Requirements
(From Life Safety Code Handbook, 2012)
7.9.3.1 Required emergency lighting systems shall be tested in accordance with one of the three options offered by 7.9.3.1.1, 7.9.3.1.2, or 7.9.3.1.3.
7.9.3.1.1 Testing of required emergency lighting systems shall be permitted to be conducted as follows:
Functional testing shall be conducted monthly, with a minimum of 3 weeks and a maximum of 5 weeks between tests, for not less than 30 seconds, except as otherwise permitted by 7.9.3.1.3(2).
The test interval shall be permitted to be extended beyond 30 days with the approval of the authority having jurisdiction.
Functional testing shall be conducted annually for a minimum of 1½ hours if the emergency lighting system is battery powered.
The emergency lighting equipment shall be fully operational for the duration of the tests required by 7.9.3.1.1(1) and (3).
Written records of visual inspections and tests shall be kept by the owner for inspection by the authority having jurisdiction.
7.9.3.1.2 Testing of required emergency lighting systems shall be permitted to be conducted as follows:
Self-testing/self-diagnostic battery-operated emergency lighting equipment shall be provided.
Not less than once every 30 days, self-testing/self-diagnostic, battery operated emergency lighting equipment shall automatically perform a test with a duration of a minimum of 30 seconds and a diagnostic routine.
Self-testing/self-diagnostic battery-operated emergency lighting equipment shall indicate failures by a status indicator.
A visual inspection shall be performed at intervals not exceeding 30 days.
Functional testing shall be conducted annually for a minimum of 1½ hours.
Self-testing/self-diagnostic battery-operated emergency lighting equipment shall be fully operational for the duration of the 1½-hour test.
Written records of visual inspections and tests shall be kept by the owner for inspection by the authority having jurisdiction.
(7.9.3.1.2, Life Safety Handbook, 2012)
(7.9.3.1, Life Safety Handbook, 2012)
7.9.3.1.3 Testing of required emergency lighting systems shall be permitted to be conducted as follows:
Computer-based, self-testing/self-diagnostic battery operated emergency lighting equipment shall be provided.
Not less than once every 30 days, emergency lighting equipment shall automatically perform a test with a duration of a minimum of 30 seconds and a diagnostic routine.
The emergency lighting equipment shall automatically perform annually a test for a minimum of 1½ hours.
The emergency lighting equipment shall be fully operational for the duration of the tests required by 7.9.3.1.3(2) and (3).
The computer-based system shall be capable of providing a report of the history of tests and failures at all times.
(7.9.3.1.2, Life Safety Handbook, 2012)

## Slide 47
HOW IS IT DONE NOW
Maintaining And Testing Emergency Lighting For Code Compliance
Here are examples of workers in compliance with the Life Safety Code 7.9.3.1.1 and 7.9.3.1.2. Emergency lighting takes mandatory monthly/yearly maintenance.

## Slide 48
HOW IS IT DONE NOW
Here is an example of an inverter sending companies automatic e-mail notifications they can access at any time in accordance with Life Safety Code 7.9.3.1.3.

## Slide 49
EACH INVERTER ALSO COMES WITH TECHNICAL SPECIFICATIONS

## Slide 50
WE TRULY HOPE THAT THE NEW CATALOGS ARE EASIER TO USE AND EXPLAIN ANY QUESTIONS THAT YOU MAY HAVE.
REMEMBER, IF YOU NEED DATA SHEETS THEY ARE AVAILABLE AS PDF’S WITH THE FIELDS READY TO FILL IN.

## Slide 51
If you have any questions please call
1.877.DSPM.POWER
(1.877.377.6769)
Thank you for watching!